## Slide 2
ultra-low freezers

## Slide 3
ultra-low freezers: -80
energy consumption
15 – 20 kWh/day
-manufacturer data
-validated by monitoring

## Slide 4
‘-70 is the new -80’

## Slide 5
‘-70 is the new -80’
chill up freezers from -80 to -70
save 2-4kW per day

## Slide 6
DOE
‘-70 is the new -80’

## Slide 7
clean freezer coils, regularly defrost freezer
save 12-25% energy
other best practices for ultra-low freezers
prolong lifetime of the freezer

## Slide 8
perform scheduled maintenance on freezers
other best practices for ultra-low freezers
prolong lifetime of the freezer

## Slide 9
remove old, unneeded samples
other best practices for ultra-low freezers
fewer samples stored, fewer freezers are needed

## Slide 10
case study: ultra-low freezers
min 7,300 kWh/year PER FREEZER
energy use
Stirling freezers
example measure
switching to Stirling freezers can save
55% min energy reduction
additional benefits
reduced HVAC related usage
reduced risk to samples

## Slide 11
transfer samples to other storage paradigms
-20 freezers
ambient temperature storage containers
other best practices for ultra-low freezers
fewer samples stored, fewer freezers are needed

## Slide 12
are there best practices that will both
reduce energy consumption
and
prolong the life of the freezer?

## Slide 13
clean freezer coils, regularly defrost freezer, change filter
save 12-25% energy
best practices for ULT freezers

## Slide 14
perform scheduled maintenance on freezers
best practices for ULT freezers
save min 10% energy

## Slide 15
remove old samples
best practices for ULT freezers
fewer samples stored, fewer freezers are needed

## Slide 16
‘-70 is the new -80’

## Slide 17
why are freezers set to -80?

## Slide 18
ultra-low temperature freezers: how they work

## Slide 19
‘-70 is the new -80’
chill up freezers from -80 to -70
save 2-4kW per day

## Slide 20
DOE
‘-70 is the new -80’

## Slide 21
what is the evidence that -70 is ok for samples?

## Slide 22
‘-70 is the new -80’
CU-Boulder
Dartmouth
Harvard
UC Davis
UC Santa Barbara
UPENN

## Slide 23
replace old freezers

## Slide 24
with more energy efficient models
ambient temperature storage containers for nucleic acids
replace old freezers

## Slide 25
how is this saving money?

## Slide 26
less energy = less stress on the compressors
= more up-time, longer freezer life

## Slide 27
possibility of financial assistance from UCSD